Project Trellis
FOSS Tools for ECP5 FPGAs
David Shah
Symbiotic EDA // Imperial College London

---
Why ECP5?
- Exciting new dev boards including TinyFPGA
- Much larger than iCE40, still simple enough for a full FOSS flow
- Cheapest FPGA per LC and readily available
- Vendor tools not as good as the “big guns”

---
ECP5 FPGA
- Up to 85k logic cells (LUT4+FF)
- Up to 3.7Mb BRAM (18Kb blocks), 156 18x18 DSPs
- Available with 3G or 5G SERDES

---
ECP5 Architecture
- Split up into tiles. Logic tiles split into 4 slices
- Slice: 2 LUT + 2FF; carry + 2FF; 16x2 RAM + 2FF; also cascade muxes
- Fixed interconnect wires
- Arcs connect wires together and are configurable or fixed (aka pip)
- All arcs and wires are unidirectional – mux topology

---
ECP5 Architecture
- More than one tile possible at a grid location
- Logic tiles contain both logic and interconnect
- Other functions split between “MIB” tiles containing functionality and “CIB” tiles containing interconnect
- Interconnect is identical for logic and other tiles

---
ECP5 Architecture

---
Current Status
- Complete bit and routing docs for logic, interconnect, BRAM and PLL tiles
- Partial docs for global network, IO and DSP tiles
- nextpnr flow supporting LUTs, FFs and IOs, can build picorv32 – proves logic docs are correct

---
Low Level Bits
- First step – pack and unpack bitstreams
- ECP5 bitstreams contain various commands
- Chip configuration structured as frames of bits
- One command configures all frames, with a CRC after each frame’s data
- Tiles are a region defined by start/end frame/bit

---
Low Level Bits
Comment header – ignored by FPGA (ASCII strings)
Preamble
Reset CRC
Check IDCODE
Dummy
Set CTRL0
Frame N-1 Data
Init Address
Load number frames

---
Low Level Bits
Frame data
CRC
Dummy

---
Frames and bits
Frame
CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC	CRC
Tile
Bit

---
Low Level Bits
- Lattice have some documentation on bitstream commands
- Trial and error needed to work out CRCs, bit ordering, etc
- Know you are good when you can round-trip to an identical bitstream

---
Low Level Bits
- Lattice include a tool to dump set bits as text
- Somewhat similar to glb files used in icestorm
- Can compare our own bitstream dumps
- Even more useful: get tile offsets in terms of frames and bits

---
Fuzzing
- Now need to work out what the bits actually do
- Created a Python library (with Boost) to access bitstreams
- Wrote a Python framework for fuzzers

---
Fuzzing
- Use Lattice ncl files to create post place-and-route designs
- Faster and very targeted
- Use a Tcl API to list wires and arcs
- Spend time looking for useful interfaces!

---
Fuzzing
- Two things to fuzz: routing and non-routing config
- Routing
  - Use Tcl to list wires in a tile and arcs on those wires
  - Create designs for each arc with only that arc, and look at bit changes
  - Normalise net names and store in database
  - 1-2 hours for a full logic tile
  - Very automated, extends to other tiles easily

---
Fuzzing
- Two things to fuzz: routing and non-routing config
- Non-routing config
  - “Word” style configuration (LUT init): create a design with each bit set and look for changes
  - “Enum” style configuration (IO type): create a design with each possible option
  - In all cases config setting and size/possible options do need to be specified manually

---
Fuzzing
Database can be rendered as HTML for manual checks
https://symbiflow.github.io/prjtrellis-db/

---
Database

---
Database
Normalised netname
Nominal position is x+3
Frame 104, bit 9
inside tile

---
Database

---
Database

---
Text Configuration
- Need to make use of & test fuzz results
- Tools to convert bitstreams to/from a text config format
- Check that output is logical for simple designs
- Check for unknown bits in larger designs

---
Text Configuration
.tile R53C71:PLC2
arc: A1 W1_H02E0701
arc: A3 H02E0701
arc: A4 H02E0501
arc: A5 V00B0000
arc: A7 W1_H02E0501
arc: B0 S1_V02N0301
arc: S3_V06S0303 W3_H06E0303
arc: W1_H02W0401 V02S0401
word: SLICEA.K0.INIT 1100110000000000
word: SLICEA.K1.INIT 1010101000000000
enum: SLICEA.CCU2.INJECT1_0 NO
enum: SLICEA.CCU2.INJECT1_1 NO
enum: SLICEA.D0MUX 1
enum: SLICEA.D1MUX 1
enum: SLICEA.MODE CCU2

---
Place and Route
- Already working on nextpnr multi-platform FOSS PnR, starting with iCE40 arch
- More on that in Clifford’s presentation next
- Next step: adding ECP5 arch to nextpnr

---
Place and Route
- iCE40 architecture uses a flat database, containing details of everything in the chip with no attempt to remove repetition
- ECP5 much larger, this would mean a database in the GB
- So we use a deduplicated database approach

---
Place and Route
- During database creation, we build a full flat database in memory using relative coordinates
- Then we split it into grid locations, and use a hash to find identical grid locations
- Identical grid locations only need their content to be stored once in the final database

---
Place and Route
- Text configuration used as an intermediate format between nextpnr and bitstream generation
- Avoids need for low level bitstream code in nextpnr

---
Next Steps – Help Wanted
- Adding PnR support for block RAM, distributed RAM and carries
- Finish DSP documentation and add synthesis and PnR support (extensions for inference)
- Creating a PLL config tool and adding PLLs to PnR
- Working on JTAG/programming tools
- Documenting advanced IO features and IO
- Improve timing documentation and create timing tool
  dave@ds0.me | GitHub prjtrellis | freenode #yosys